## Slide 1: CSCI E-96 Data Mining, Discovery and Exploration Steaming Analytics
Steve Elston

## Slide 2
Are analytics always computed in batch
No!
Data often arrives in streams
  Sensor data
  Capital markets data
  E-commerce purchases
  Logistics
  Etc.
Analytics must be updated as data samples arrives
Streaming Analytics

## Slide 3
Difficulties with streaming analytics
Data volumes can be massive
Example – relatively small scale
  US Geological Survey maintains about 13,500 stream gages
  Average of 4 types of sensors per station
  Each measurement is 4 bytes - 16 bytes total per sample
  Each gage collects data sample every 15 mins
  Data uploaded every 4 hours – 6 sets of measurements per day – 1,536 bytes
  Total of 5.4 M bytes per day for network
  2 G bytes per year for network
Streaming Analytics

## Slide 4
Difficulties with streaming analytics
Data volumes can be massive
2nd Example – Large scale
  Power company with real-time energy monitoring of 107 customer sites
  4 bytes every 10 ms per customer
  34,560 bytes per customer per day
  346 M bytes total per day
  126 T bytes per year
Streaming Analytics

## Slide 5
Difficulties with streaming analytics
Results must be updated as new values arrive
How to treat older values?
  How much should older values weight in the analytic results?
  How much storage capacity is required for the history?
Can we filter massive streams?
  Reduce volume of stream data to process
  Use filtered values to update analytics
Can we compute and store only summary statistics?
  Massive reduction in volume
Streaming Analytics

## Slide 6
Components of stream analytics
Multiple input streams – potentially different data types
Real-time stream processor
Real-time stream analytics output
Limited working storage for real-time processing
Ad-Hoc query capability – typically limited
Long-term archival storage
Streaming Analytics
Processor
Limited
Working
Storage
. . . 1, 5, 2, 7, 0, 9, 3
. . . a, r, v, t, y, h, b
. . . 0, 0, 1, 0, 1, 1, 0
time
Streams Entering.
Each is stream is composed of elements/tuples
Ad-Hoc
Queries
Output
Archival
Storage
Standing
Queries

## Slide 7
Push most processing to the periphery of network
Network bandwidth is major limitation for large networks
  Consider IoT application with 100,000 sensors
  At 1 sec sampling interval reporting rate is 360 M samples (messages) per hour
  Statistic aggregated to 10 min reporting rate is 600 K samples (messages) per hour
Many peripheral devices have considerable processing power
  We can take advantage of these idle capacity
  Greatly reduce load on networks and central processing
Processing of Stream Data

## Slide 8
Memory requirements for stream analytics
Cannot store all history of streams in main memory!
  At large scale cannot even store all history to disk
We need a better approach!
Some ideas:
  Delta coding: Only update when there is substantial change
  Moving window: Compute statistic for each window position
  Decay window: compute statistic down-weighting older event values
  Bloom filter: uses hash to represent occurrence of events
  Other hash algorithms: use hashes to approximate counts
Memory Requirements

## Slide 9
Delta coding only transmits and processes values with significant differences
Example: consider a large network of sensors (IoT)
  Values at most sensors do not change most of the time
  Temperature has not changed significantly
  Nothing moving in or out of image
  Current in transmission line has not changed
  Etc.
Delta coding restricts transmission, processing and storage to significant changes (deltas)
  A threshold determines significance of change
  Threshold values are solution specific
Delta Coding

## Slide 10
Delta coding moves filtering and initial processing to periphery of network
Example: Measuring flow in pipe network
  100,000 flow sensors sampling every 1-sec with +/-3% standard error
  Set threshold and only report if change more than +/-3% of moving average
  Report moving average for last 5 min, not 1-sec sampling
  Can reduces network traffic and processing by orders of magnitude
Example: Security camera watching gate
  Image transmission expensive at raw 50-60 frames per second
  Threshold on object greater than some number of pixels moving in frame
  Reduces transmission, processing and storage by many orders of magnitude
Delta Coding

## Slide 11
Compute and store summary statistics from moving window
Need to update the analytic as new values received
Naïve approach: maintain an estimate in a window?
On update
  Add new observation to the end of window
  Remove old observation from beginning of window
  Compute and store new estimate of statistic
But, this requires keeping all observations within the window in main memory
Does not scale well
Moving Window Analytics

## Slide 12
Compute and store summary statistics from moving window
Better approach to updating statistic with moving window
On update:
  Add new observation to the beginning of window
  Remove old observation from end of window
Compute and store new estimate of statistic:
  After a fixed number of observations received
  Or at fixed time interval
Can be significant compression of data
  But may not scale well for large scale
  Cannot store continuous history
Moving Window Analytics

## Slide 13
Compute and store summary statistics from moving window
Window sampling acts as a low-pass filter
  High frequencies are filtered
  Low frequencies and trend retained
Length of window determines bandwidth
  Longer window only pass lower frequencies
  Shorter window pass higher frequencies
  Can analyze bandwidth with impulse response methods – beyond the scope of this course
Window choice is critical
  Short enough to pass important changes in signals – sufficient bandwidth
  Long enough to compress data
Moving Window Analytics

## Slide 14
Exponential decay
Need to update the analytic as new values received
Is there an alternative to moving windows?
Yes, exponential decay methods
  Past values are exponentially down-weighted in time
  Estimates of a statistic are updated with new observations
  Computationally efficient
Exponential Decay Analytics

## Slide 15
Family of exponential smoothing algorithms
Family of algorithms known as the Holt-Winters methods
First order exponential smoother
  Smooths random (white) noise
  Acts as a low-pass filter
Second order model
  Known as double exponential smoothing
  Includes a trend term
Third order model
  Known as triple exponential smoothing
  Accounts for seasonal (periodic) component
Exponential Decay Analytics

## Slide 16
Formulation of first order exponential smoother
Start with the initial conditions – initial observation and initial smoothed output :
Formulate the update at time with new observation :
Applying some elementary calculus we can formulate the above in terms of decay constant for a sampling period :
1
Exponential Decay Analytics

## Slide 17
Formulation of first order exponential smoother
Start with the initial conditions – initial observation and initial smoothed output :
Formulate the update at time with new observation :
Applying some elementary calculus we can formulate the above in terms of decay constant for a sampling period :
1
Exponential Decay Analytics

## Slide 18
Sampling frequency
Consider the decay constant for a sampling period :
1
Choice of determines the bandwidth:
  Large shorter memory, higher bandwidth
  Small longer memory, lower bandwidth
Bandwidth and sampling
  High bandwidth high sampling rate, less compression
  Low bandwidth low sampling rate, higher compression
Exponential Decay Analytics

## Slide 19
Second order exponential smoothing
Second order exponential smoothing accounts for trend
Start with initial conditions for smoothed values and smoothed slope
The update at each time step, with smooth coefficient and slope smoothing coefficient
Third order exponential smoothing adds seasonal term
Exponential Decay Analytics

## Slide 20
Often need to exclude events
Messages from IP addresses not on an authorized list
Is the originating phone one of our accounts?
Etc.
Or, determine if an event already occurred perviously?
The majority of traffic is often filtered
Filtering Event Data

## Slide 21
Filtering streaming data
How can we filter a stream of events?
  Hash table look-up?
  B-tree structure?
Above works at small scale
  Need to store hash for each allowed value or state
Must maintain lookup in main memory for speed
A Bloom filter is a highly space-efficient lookup
  No false negative event
  Some probability of false positive – hash collision
Filtering Event Data

## Slide 22
Memory requirements for stream analytics
We need a better approach!
Some ideas:
  Decay window: compute stream statistics
  Bloom filter: filter stream data
  Count distinct elements: home many events of different types in a stream
Categorical Data